## Slide 1
Reverse Engineering
of Rocket-Chip
December 8-10 | Virtual Event
ASSOCIATE MEMBER CHIPS ALLIANCE
COMMUNITY ORGANIZATION MEMBER RISCV

## Slide 2
December 8-10 | Virtual Event
Reverse Engineering of Rocket-Chip
Dr Roomi Naqvi
Director
MERL-PAKISTAN
#RISCVSUMMIT

## Slide 3: To be covered
Goals
  To reduce the complexity of Rocket-Chip
  Extend to add Vector extension.
Complexity of Task
  Number of Modules, functions, Number of lines, objects etc
  Scala Vs Chisel
Software Methodology
  UML – Class diagrams
  Software spec to Micro-architecture spec
Block
  Shows how the methodology was employed
Future Research
  Parameterize-able Micro-Architecture
  Parameterize-able I/O interface

## Slide 4
Motivation and Scope
To provide a detailed elaboration and establish an understanding of Rocket-core to generate a customized System on Chip (SoC). Moreover, to modify and enhance a module based on customized specifications later.
To come up with a hardware insight by mapping it to blocks of code which highlights the wiring and back tracing of input/output by means of variables. Hardware mapping provides a connection in the entire workflow between software and hardware.
The Microarchitecture Specification (MAS) Document developed by MERL-UIT aims to present a detailed description of Rocket-chip core and its micro-architecture to the features additional representations such as block diagrams and flowcharts.

## Slide 5: Methodology
We decode basic modules of rocket chip by taking understanding of its code with the help of Scala and Chisel expertise.
We convert these modules code understanding into flow charts and start making Micro Architecture Specification (MAS) documentation.
We make flow charts for different modules of Rocket Chip. After completion of flow charts, we make block diagrams of Rocket Chip modules according to its configuration pin in and out

## Slide 6: Hardware Insight of Rocket Chip

## Slide 7: ROCKET-CHIP Overview
Rocket-chip is an SoC generator framework and can be configured with single or multiple processor cores, caches, on-chip busses, individual buses and bus interconnections. All these devices are a part of SoC which is referred as a sub system.
A full chip however needs some additional devices which include (UART, GPIO etc.) that have not been accommodated in the Rocket-chip repository which can be viewed at sifive/sifive-blocks.
To add these modules we have to understand the diplomacy of rocket chip. Diplomacy is a Scala run-time parameter negotiation and generation mechanism. It is implemented in chisel language and heavily leverages the software engineering features provided by Chisel (Scala).
Rocket-chip Is coded in Scala language and one of its library Chisel. Chisel is used for hardware design that enables advanced circuit generation and reuse of designs for both ASIC and FPGA digital logic designs.
When we compile Chisel code it converts into Firrtl. Firrtl which is an intermediate representation (IR) developed as a medium for writing circuit-level transformations for digital circuits.
Once Chisel is converted into Firrtl, it converts into Verilog which we further uses to map it on FPGA Board.

## Slide 8: ROCKET-CHIP Micro-Architecture

## Slide 9: Rocket-chip Modules Description
Module | Description
PTW | Page table is used to access the virtual memory To Allocate/de-allocate memory in same size chunks (pages).A hardware page table walker (PTW) walks the page table
Priority Encoder | Priority Encoders take all of their data inputs one at a time and converts them into an equivalent binary code at its output
EPC | The Exception Program Counter (EPC) is used to store the address of the instruction that was executing when the exception was generated. The size of the EPC register depends upon the width of the ISA which can be of [31:0] / [63:0]
NPC | New Program Counter (NPC). It increments +4 in current PC and store in register. The size of the NPC register depends upon the width of the ISA which can be of [31:0] / [63:0]
NPC-Gen Modules Description
Module | Description
ICache | The Instruction Cache acts as a buffer memory between external memory and the core processor. Size of the Icache sets, ways and block can be configured from the config.scala file in subsystem directory of Scala files. Size of ICache is calculated by: nWays x nSets x blockBytes
BTB | Branch Target Buffer (BTB) is a cache-like component in processors that is used for branch prediction. The main concept of the BTB is to store the program counter (PC) of a branch instruction, and also the PC of the target of the branch. The bit size of branch prediction is [1:0].
TLB | Translation Lookaside Buffer (TLB) is memory cache which is used to keep track of recently used transactions and reduce the time taken to access a user memory location.TLB is connected with rocket chip PTW and work as cache for PTW
Fetch Modules Description

## Slide 10
Module | Description
Register File | Registers are temporary storage locations that hold data and addresses. The width of the rocket chip file register is fixed by the xlen variable between [31:0] / [63:0]
Instruction buffer | Ibuffer is a temporary register where the opcode of the currently fetched instruction from instruction memory is stored. The RV32 / RV64 instruction opcode is [6:0] bits. The Ibuffer size is set for ISA 32 and 64.
RVC | This Module holds RISC-V Compressed (C-Extension) Instructions. To use the RISC V Compressed instructions, useCompressed [Bool], which is in the rocket chip config file, should be true.
Immediate Generation | Immediate generation module generates immediate for instructions of RISC V. This module is located in RocketCore.scala and returns immediate bits depending upon the size of ISA [31:0] / [63:0]
Instruction Decode | This module decodes instructions for RISC V which come from Instruction Memory. Width of the instruction can be parameterizable RISCV[31:0] / RISCV[63:0].
Scoreboard | Scoreboards are designed to control the flow of data between registers and multiple arithmetic units in the presence of conflicts caused by hardware resource limitations (structural hazards) and by dependencies between instructions (data hazards).Scoreboard module lies in RocketCore.scala.
CSR | Control and Status Register (CSR) is a register in many central processing units that are used as storage devices for information about instructions received from machines.The width of the CSRs is parameterizable and can be between [31:0] / [63:0] depending on the ISA width.
Breakpoint | A breakpoint is a location in executable code at which the operating system stops execution and breaks into the debugger. This allows you to analyze the target and issue debugger commands.
Decode Modules Description

## Slide 11
Module | Description
Multiplier | This module is present inside the rocket core execute stage and is used to perform M-Type Instructions. Multiplier operation is parameterizable depends upon the xLen width (Width of the operands of Multiplier). xLen can be [31:0] or [63:0].
ALU | An arithmetic logic unit (ALU) is a digital circuit used to perform arithmetic and logic operations in Rocket Core. ALU operation is parameterizable depends upon the xLen width (Width of the operands of ALU). xLen can be [31:0] or [63:0]
Execute Modules Description
Module | Description
Memory | This module is for accessing data from rocket core memory with the use of load instructions
HellaCache | HellaCache is the acronym of Level 1 Data cache. L1 Dcache directly built into the microprocessor, which is used for storing the microprocessor's recently accessed information, thus it is also called the primary cache. The size of the cache depends upon the width of the ISA.
HellaCache Arbiter | This module is for accessing L1 Dcache (HellaCache), by means of requests generated from other modules for read and write operations.
PMP | Physical Memory Protection (PMP) is a part of the RISC-V Privileged Architecture Specification which describes the interface for a standard RISC-V memory protection unit. The PMP defines a finite number of PMP regions which can be individually configured to enforce access permissions to a range of addresses in memory
AMO-ALU | This module is used to perform the A Extension RISCV operations. To use the Rocket Core Atomic ALU module, useAtmoics [Bool],which is in the rocket chip config file, should be true.
Dcache | This Module is used to hold the data for temporary period of time.Size of the Dcache sets, ways and block can be configured from the config.scala file in subsystem directory of Scala files. Size of DCache is calculated by: nWays x nSets x blockBytes.
Scratchpad | (SPRAM) is a high-speed internal memory directly connected to the CPU core and used for temporary storage to hold very small items of data for rapid retrieval. To add the scratchpad in our SoC we need to call the scratchpad class in our config file which lies in system directory of Scala.
WB | This module performs the Write back operation in the Rocket core. This module will write the data into the rocket core memory or register file of rocket core.The writeback stage of rocket core is defined in Rocketcore.scala file
Memory/ Write-Back Modules Description

## Slide 12: Software Insight of Rocket Chip

## Slide 13: Code Complexity
The complexity of code of Rocket-chip is high, because it contains 372 files in 73 directories, after the submodules the numbers increase to 151,613 files in 8,625 directories and after running the build script to generate an SoC the numbers grow to 185,049 files in 10,780 directories1.
The code of Rocket-chip is extensive and complex because it contains 328 source files of Scala in 23 directories, and 33,427 total lines of Scala code.
Another problem faced was that Rocket chip includes many irrelevant variable names and non elaborated statements, further contributing to process confusion, raising the decoding complexity and making it difficult to understand the inputs / outputs of the hardware.
Lack of understandability and comprehension concludes to difficulty in modifying Rocket-core or its component as for customized requirements.
1 Durrum, J., Bryant, A. and Porter, J., 2019. Reverse Engineering RISC-V Generator-Based Designs for Trust and Assurance. AFRL/RYDT WPAFB United States.

## Slide 14: Code Hierarchy
Branch Target Buffer (BTB)
Instruction Buffer

## Slide 15: Class Diagram Explanation
Class name IBuf
Class name BTBResp
Public Attributes of class IBuf
Public Attributes of class BTBResp
Public Methods of class BTBResp
Class IBuf has an instance of BTBResp initialized by the variable ibufBTBResp
Class BTBResp is inherited from its parent class, therefore it uses the methods of its parent class.

## Slide 16: Object Oriented Code of Rocket-Chip
Inheritance
Polymorphism
Encapsulation
Abstraction
Abstraction is achieved by abstract keyword, creating an abstract trait of DecodeConstants
Private access modifier is used to encapsulate/hide method ‘access’ from other extended classes
Keyword extend is used to extend/inherit the PMP class with parent class PMPReg
Keyword override is used to override method getOMSRAMs, which is already defined in the parent class.

## Slide 17: Put it all Together (Hardware and Software)

## Slide 18
Code Explanation and Back-tracing
by Flowcharts and Block Diagram
Class RegFile is initiated with three parameters n, w and zero having type Int and Bool.
This class creates register file of rocket chip.
Mem function is used to create memory where n= depth/entries of memory and w= width of memory.
In the class RegFile, a private method named access is defined for accessing the register file data by taking the address as its input parameter.
Private variable reads calculates the address which will be used to read the data..
Private variable canRead is defined as true for read state.
For write state canRead will be false.
“read” method is defined in class RegFile to read data from register file. It takes addr as parameter.

## Slide 19
regAddrMask [n] = depth/entry of register file memory
xLen[w] = width of registers [31:0]/[63:0]
raddr = address of register [4:0]
data = data to be written in the register [31:0]/[63:0]
reads.lasts._2 = data read from register file address [31:0]/[63:0]
rdata = data output from register file [31:0]/[63:0]

## Slide 20
Class Parameters is imported from directory config of rocket-chip
Class CoreModule is imported from directory tile of rocket-chip
Input/Output of class ALU are defined
Object ALU is defined
ALU operation bits are defined in method SZ_ALU_FN
ALU operations are defined
Importing all properties of Chisel

## Slide 21
Class ALU has three inputs and three outputs
ALU I/O | Description
dw | Data width is an input of ALU which can be 32bit or 64 bit
fn | fn (ALU operation Bits) as input, width is predefined by 4
in2 | Operand B input, here xLen can be changed to 32 or 64bits
in1 | Operand A input, here xLen can be changed to 32 or 64bits
out | It is the ALU result output for logical operators, generated by the ALU
adder_out | It is the ALU result output for mathematical operators, generated by the ALU
cmp_out | Branch output whether branch condition True or False
Deep Dive into Rocket-ALU

## Slide 22
In Rocket core ALU, this code block performs addition and subtraction operations.
The result of the addition / subtraction operation performed by ALU is output by adder out
Variable in2_inv is initialized with Mux function which has parameters, isSub function with parameter io.fn as selector, Not of io.in2 as input1 of Mux, and io.in2 as input2 of Mux
Variable in1_xor_in2 is initialized with io.in1 XOR’ed ( ^ ) with in2_inv.
Io.adder_out is wired to io.in1 + in2_inv + isSub of io.fn

## Slide 23
dw = datawidth [31:0]/[63:0]
fn = ALUop bit as input [3:0]
In1 = Operand B of ALU as input [31:0]/[63:0]
In2 = Operand A of ALU as input [31:0]/[63:0]
out = ALU result output for logical operators [31:0]/[63:0]
adder_out = ALU result output for mathematical operations [31:0]/[63:0]
Cmp_out = Branch result output [Bool]

## Slide 24: MAS Document of Rocket Chip

## Slide 25: How did we do it?
Using Reverse Engineered MAS Document, which includes in depth knowledge of all Rocket-Chip modules

## Slide 26: Rocket Core MAS Documentation
This MAS Document offers in-depth knowledge of Rocket-Chip SoC modules.
Using Block Diagrams, Class Diagrams, Flowcharts, and describing all the keywords found in the code, description of modules is achieved.
This MAS Document is essential for those who have fundamental knowledge of Scala, CHISEL and SoC hardware.
Only the keyword name is used in the MAS Document, but its meaning is stated in the keywords Appendix-Scala & CHISEL.

## Slide 27: Aghaz(آغاز) SoC The Beginning

## Slide 28: Specifications of Aghaz(آغاز) SoC
RV-32 (32-bit)
I, M & C extensions
64-KB Instruction and Data Cache
CLINT
PLIC
Privileged( Machine)

## Slide 29: Configuring Aghaz Core in Rocket-Chip
Rocket Core parameters
Data Cache parameters
Instruction Cache parameters
Class named AghazCore, contains the configurations for the core level functionality. This class is created in Rocket-chip/src/main/scala/subsystem/Config.scala
Path to Default Configuration Scala File

## Slide 30: Configuring RV32IMC Core
RocketCoreParams has the parameters for configuring our Core.
We added MulDiv(Multiplier) with MulDivParmas, having default values, in the RocketCoreParams, in order to enable M extension in our Core.
We updated the value of useAtomics to false, to disable A extension.
The number of cycles per multiplication.
mulEarlyOut will make the multiplier's latency data-dependent, i.e., it will take fewer cycles to multiply small numbers than large ones.
divEarlyOut is analogous to mulEarlyOut (smaller numbers divide more quickly than larger ones).
We updated fpu (Floating-Point unit) to None, to disable F and D extensions in our core.

## Slide 31: Aghaz Core Params (Core)
In the RocketCoreParams, useCompressed is true, means C extension is enabled by default.
Extension I is the base extension and is supported by default as well.
Hence, Aghaz core is configured to support I, M and C Extensions.
useCompressed | true | useCompressed is for C-extension, it is true by default, means our Core will have C-extension enabled implicitly.

## Slide 32: Configuring the cache and dcache in Aghaz Core
Dcache has DCacheParams, which set the parameters for Data Cache.
Similarly, ICache has ICacheParams, which are parameters for the InstructionCache configuration.

## Slide 33: Data Cache Parameters
Parameters | Value | Description
nMSHRs | 0 | There are 0 MSHRs (Miss Status Handling Registers) in Instruction Cache
nWays | 16 | There are 16 Ways of Cache in DCache
nSets | 64 | There are 64 Sets of Cache in DCache
blockBytes | 64 (evaluated) | There are 64 blockBytes in DCache
Instruction Cache Parameters
Parameters | Value | Description
nWays | 4 | There are 4 Ways of Cache in ICache
nSets | 256 | There are 256 Sets of Cache in ICache
blockBytes | 64 (evaluated) | There are 64 blockBytes in ICache
Size of DCache is calculated by: nWays x nSets x blockBytes (16 x 64 x 64 == 64KB)
Size of ICache is calculated by: nWays x nSets x blockBytes (4 x 256 x 64 == 64KB)

## Slide 34: Blocks of Core
Aghaz Core provides extensions for I, M and C with 32bit compatibility.

## Slide 35: How did we know, which parameter is doing what?
The MAS Document describes the parameters, their description, and the modules that are managed by that parameter.

## Slide 36: Blocks of Tile
Rocket-Tile of Aghaz SoC contains Aghaz Core, Branch Target Buffer, L1 Icache & DCache of 64-KB

## Slide 37: Initializing Aghaz Core to Default Configuration
The class called oldDefaultConfig is inherited by the class Config.
The Class Config (Parent Class) includes the key configurations, from which all configurations must be inherited.
The AghazCore object is generated as a parameter with ’1’ indicating that there is only one(1) core in our AghazCore.
The AghazCore object is further added to the WithCoherentBusTopology object, which includes configurations for the Bus level.
These objects are further added by the newBaseConfig object, which contains the base configurations.
Default Configuration is created in Rocket-chip/src/main/scala/system/Config.scala
Path to Default Configuration Scala File

## Slide 38: Customizing AghazCore to 32-bit Configuration

## Slide 39: Blocks of SoC

## Slide 40: At this point our Aghaz SoC is successfully configured and ready to be built.

## Slide 41: Configuring an SoC to your Requirements in a quick process by means of this MAS Document

## Slide 42: Acknowledgements This Document was made possible with the counselling, guidance and support of Dr.Roomi Naqvi, Dr Ali Ahmed Ansari, and Farhan Ahmed Karim. Without their encouragement and guidance, this could not be possible. This Document was created under the Lead of Uzair Khan, along with the team of collaborators/ interns under him that gave their level best under the supervision of such experienced mentors.
Team Members
Waleed Waseem
Shahzaib Kashif
Talha Ahmed
Mohsin Raza
Muhammad Shahzaib
Syeda Fizza Jaffery
Almas Ibrahim
Ubab Nadeem

## Slide 43
December 8-10 | Virtual Event
Thank you for joining us.
Contribute to the RISC-V conversation on social!
#RISCVSUMMIT @risc_v

## Slide 44
https://docs.boom-core.org/en/latest/sections/intro-overview/rocket-chip.html