## Slide 1
Reverse Engineering
of Rocket-Chip
December 8-10 | Virtual Event

## Slide 2
December 8-10 | Virtual Event
Reverse Engineering of Rocket-Chip
Dr. Roomi Naqvi, MERL Researchers & Students
Director
MERL-PAKISTAN
#RISCVSUMMIT

## Slide 3: Outline
Motivation and Scope
  Reverse Engineer Rocket-Chip for the generation of System on Chip (SOC) utilizing the modules of Rocket-Chip
Rocket Chip Basics
De-constructing the Software Architecture of Rocket Chip
From Rocket Chip to Aghaaz Chip
  Mapping Software to Micro architecture and software Spec
Future Research
  Integrate devices to the Rocket Chip SOC that are not available in the rocket-chip repository which includes GPIO, i2c, jtag etc.
  Extend to include the Vector Extensions etc ..

## Slide 4
Motivation and Scope
Develop an understanding of Rocket-core and use Rocket-Chip to generate a customized System on Chip (SoC). Moreover, to modify and enhance a module based on customized specifications later.
Provide a hardware insight by mapping it to blocks of code which highlights the wiring and back tracing of input/output by means of variables. Hardware mapping provides a connection in the entire workflow between software and hardware.
The Microarchitecture & Software Specification (MASS) Document developed by MERL-UIT aims to present a detailed description of Rocket-Chip Core and its micro-architecture with additional representations such as block diagrams and flowcharts.

## Slide 5: Methodology
Decoded basic modules of Rocket-Core by understanding its code with the help of Scala and Chisel expertise.
Represented the code flow through flow charts, class diagram and block diagrams.
These diagrams and understandings were then ported into the Micro Architecture Specification (MAS) document.
Used the MAS Document together with Rocket-Chip generator to generate Aghaz(آغاز) SoC

## Slide 6: Basics of Rocket-Chip

## Slide 7: Rocket-Chip Overview
Rocket-Chip is a configurable SoC generator framework which creates a system of single or multiple processor cores, caches, on-chip busses, individual buses and bus interconnections
Rocket-Chip framework is implemented in Chisel: an open-source hardware construction language embedded in scala. Chisel enables generation of parameterizable digital hardware circuits
Chisel generated circuits are then transformed into an intermediate representation (IR) thru FIRRTL. This representation is then further transformed by the FIRRTL parser into Verilog
An SoC however needs some additional devices which include (UART, GPIO etc.) that have not been accommodated in the Rocket-Chip repository which can be viewed at sifive/sifive-blocks.
To add these modules we have to understand the diplomacy of Rocket-Chip. Diplomacy is a Scala run-time parameter negotiation and generation mechanism. It is implemented in Chisel language and heavily leverages the software engineering features provided by Chisel (Scala).

## Slide 8: Rocket-Core Micro-Architecture

## Slide 9: Rocket-Core Modules Description
Module | Description
PTW | Page table is used to access the virtual memory.nL2TLBEntries parameter is used by Rocket-Chip PTW for controlling TLB entries.
Priority Encoder | Priority Encoders take all of their data inputs one at a time and converts them into an equivalent binary code at its output. Rocket-Chip Priority Encoder is taking pins as input, from BTB and EPC( from all stages) to select the value of NPC.
EPC | The Exception Program Counter (EPC) is used to store the address of the instruction that was executing when the exception was generated. The size of the EPC register depends upon the width of the ISA which can be of [31:0] / [63:0].
NPC | New Program Counter (NPC)is used to increments +4 in current PC and store in register. The size of the NPC register depends upon the width of the ISA which can be of [31:0] / [63:0].
NPC-Gen Modules Description
Module | Description
ICache | The Instruction Cache acts as a buffer memory between external memory and the core processor. In Rocket-Chip size of the ICache sets, ways and block can be configured from the config.Scala file in subsystem directory of Scala files. Size of ICache is calculated by: nWays x nSets x blockBytes
BTB | Branch Target Buffer (BTB) is a cache-like component in processors that is used for branch prediction. The main concept of the BTB is to store the program counter (PC) of a branch instruction, and the PC of the target of the branch. The bit size of branch prediction is [1:0].
TLB | Translation Lookaside Buffer (TLB) is a memory cache which is used to keep track of recently used transactions and reduce the time taken to access a user memory location’s .It is connected with Rocket-Chip PTW and work as cache for PTW.TLB entries is controlled by PTW of Rocket-Chip.
Fetch Modules Description

## Slide 10
Module | Description
Register File | Registers are temporary storage locations that hold data and addresses. The width of the rocket-Chip file register is fixed by the xlen variable between [31:0] / [63:0].
Instruction buffer | Ibuffer is a temporary register where the opcode of the currently fetched instruction from instruction memory is stored. The RV32 / RV64 instruction opcode is [6:0] bits. The Ibuffer size is set for ISA 32 and 64.
RVC | This Module holds RISC-V Compressed (C-Extension) Instructions. To use the RISC V Compressed instructions, useCompressed [Bool], which is present in Rocket-Chip config file, should be true.
Immediate Generation | Immediate generation module generates immediate for instructions of RISC V. This module is located in RocketCore.scala and returns immediate bits depending upon the size of ISA [31:0] / [63:0].
Instruction Decode | This module decodes instructions for RISC V which come from Instruction Memory. Width of the instruction can be parameterizable depending upon the ISA width RISCV[31:0] / RISCV[63:0].
Scoreboard | Scoreboards are designed to control the flow of data between registers and multiple arithmetic units in the presence of conflicts caused by hardware resource limitations (structural hazards) and by dependencies between instructions (data hazards).Scoreboard module lies in RocketCore.scala.
CSR | Control and Status Register (CSR) is a register in many central processing units that are used as storage devices for information about instructions received from machines.The width of the CSRs is parameterizable between [31:0] / [63:0] depending on the ISA width.
Breakpoint | A breakpoint is a location in executable code at which the operating system stops execution and breaks into the debugger. This allows you to analyze the target and issue debugger commands.
Decode Modules Description

## Slide 11
Module | Description
Memory | This module is for accessing data from Rocket-Core memory with the use of load instructions
HellaCache | HellaCache is the acronym of Level 1 Data cache. L1 Dcache directly built into the microprocessor, which is used for storing the microprocessor's recently accessed information, thus it is also called the primary cache. The size of the cache depends upon the width of the ISA.
HellaCache Arbiter | This module is for accessing L1 Dcache (HellaCache), by means of requests generated from other modules for read and write operations.
PMP | Physical Memory Protection (PMP) is a part of the RISC-V Privileged Architecture Specification which describes the interface for a standard RISC-V memory protection unit. The PMP defines a finite number of PMP regions which can be individually configured to enforce access permissions to a range of addresses in memory
AMO-ALU | This module is used to perform the A Extension RISCV operations. To use the Rocket-Core Atomic ALU module, useAtmoics [Bool],which is in the rocket-Chip config file, should be true.
Dcache | This Module is used to hold the data for temporary period of time.Size of the Dcache sets, ways and block can be configured from the config.scala file in subsystem directory of Scala files. Size of DCache is calculated by: nWays x nSets x blockBytes.
Scratchpad | (SPRAM) is a high-speed internal memory directly connected to the CPU core and used for temporary storage to hold very small items of data for rapid retrieval. To add the scratchpad in our SoC we need to call the scratchpad class in our config file which lies in system directory of Scala.
WB | This module performs the Write back operation in the Rocket-Core. This module will write the data into the Rocket-Core memory or register file of Rocket-Core. The writeback stage of Rocket-Core is defined in Rocketcore.scala file
Memory/ Write-Back Modules Description
Module | Description
Multiplier | This module is present inside the Rocket-Core execute stage and is used to perform M-Type Instructions. Multiplier operation is parameterizable depends upon the xLen width (Width of the operands of Multiplier). xLen can be [31:0] or [63:0].
ALU | An arithmetic logic unit (ALU) is a digital circuit used to perform arithmetic and logic operations in Rocket-Core. ALU operation is parameterizable depends upon the xLen width (Width of the operands of ALU). xLen can be [31:0] or [63:0]
Execute Modules Description

## Slide 12: De-constructing Software Architecture Rocket-Chip

## Slide 13: Code Complexity
Rocket Chip SoC framework contains ~372 files in ~73 directories, after the submodules the numbers increase to 151,613 files in 8,625 directories and after running the build script to generate an SoC the numbers grow to 185,049 files in 10,780 directories1.
Rocket Chip SoC implementation consists of 328 source files of Scala in 23 directories, and 33,427 total lines of Scala code
No documentation and lack of comments in the scala code makes it very difficult to get a good understanding of the Rocket Chip implementation
Scala code uses variable names and complex object oriented code, which further contributes to complexity and making it difficult to understand the implementation
1 Durrum, J., Bryant, A. and Porter, J., 2019. Reverse Engineering RISC-V Generator-Based Designs for Trust and Assurance. AFRL/RYDT WPAFB United States.

## Slide 14: Our Approach
Object Oriented Programming (OOP) and high-level Functional Programming concepts helps in understanding the code of Rocket-Chip.
Code complexity is reduced by means of Flowcharts, UML Class Diagrams and Block Diagrams of each modules of Rocket-Chip
Assigned a team of undergraduate CS students to go thru the code line-by line
Develop a detailed document fusing the software architecture of the implementation with the Mico-architecture of Rocket Chip (MASS)

## Slide 15: Code Hierarchy
Branch Target Buffer (BTB)
Instruction Buffer

## Slide 16: Class Diagram Explanation
Class name IBuf
Class name BTBResp
Public Attributes of class IBuf
Public Attributes of class BTBResp
Public Methods of class BTBResp
Class IBuf has an instance of BTBResp initialized by the variable ibufBTBResp
Class BTBResp is inherited from its parent class (BtbBundle), therefore it uses the methods of its parent class.

## Slide 17: Object Oriented Code of Rocket-Chip
Inheritance
Polymorphism
Encapsulation
Abstraction
Abstraction is achieved by abstract keyword, creating an abstract trait of DecodeConstants.
Private access modifier is used to encapsulate/hide method ‘access’ from other extended classes.
Keyword extend is used to extend/inherit the PMP class with parent class PMPReg.
Keyword override is used to override method getOMSRAMs, which is already defined in the parent class.

## Slide 18: Putting it all Together (MASS: Hardware and Software)

## Slide 19
Code Explanation and Back-tracing
by Flowcharts and Block Diagram
Class RegFile is initiated with three parameters n, w and zero having type Int and Bool.
This class creates register file of rocket-Chip.
Mem function is used to create memory where n= depth/entries of memory and w=width of memory.
In the class RegFile, a private method named access is defined for accessing the register file data by taking the address as its input parameter.
Private variable reads calculates the address which will be used to read the data.
Private variable canRead is defined as true for read state.
For write state canRead will be false.
“read” method is defined in class RegFile to read data from register file. It takes addr as parameter.

## Slide 20
regAddrMask [n] = depth/entry of register file memory
xLen[w] = width of registers [31:0] / [63:0]
raddr = address of register [4:0]
data = data to be written in the register [31:0] / [63:0]
reads.lasts._2 = data read from register file address [31:0] / [63:0]
rdata = data output from register file [31:0] / [63:0]

## Slide 21
Class Parameters is imported from directory config of rocket-chip
Class CoreModule is imported from directory tile of rocket-chip
Input/Output of class ALU are defined
Object ALU is defined
ALU operation bits are defined in method SZ_ALU_FN
ALU operations are defined
Importing all properties of Chisel

## Slide 22
Class ALU has three inputs and three outputs
ALU I/O | Description
dw | Data width is an input of ALU which can be 32bit or 64 bit
fn | fn (ALU operation Bits) as input, width is predefined by 4
in2 | Operand B input, here xLen can be changed to 32 or 64bits
in1 | Operand A input, here xLen can be changed to 32 or 64bits
out | It is the ALU result output for logical operators, generated by the ALU
adder_out | It is the ALU result output for mathematical operators, generated by the ALU
cmp_out | Branch output whether branch condition True or False
Deep Dive into Rocket-ALU

## Slide 23
In Rocket-Core ALU, this code block performs addition and subtraction operations.
The result of the addition / subtraction operation performed by ALU is outputby adder out
Variable in2_inv is initialized with Mux function which has parameters, isSub function with parameter io.fn as selector, Not of io.in2 as input1 of Mux, and io.in2 as input2 of Mux
Variable in1_xor_in2 is initialized with io.in1 XOR’ed ( ^ ) with in2_inv.
Io.adder_out is wired to io.in1 + in2_inv + isSub of io.fn

## Slide 24
dw = datawidth [31:0]/[63:0]
fn = ALUop bit as input [3:0]
In1 = Operand B of ALU as input [31:0]/[63:0]
In2 = Operand A of ALU as input [31:0]/[63:0]
out = ALU result output for logical operators [31:0]/[63:0]
adder_out = ALU result output for mathematical operations [31:0]/[63:0]
Cmp_out = Branch result output [Bool]

## Slide 25: How did we do it?
Using Reverse Engineered MAS Document, which includes in depth knowledge of all Rocket-Chip modules.

## Slide 26: Rocket-Core MASS Documentation
This Micro-Architecture and Software Specification Document offers in-depth knowledge of Rocket-Chip SoC modules.
Using Block Diagrams, Class Diagrams, Flowcharts, and describing all the keywords found in the code, description of modules is achieved.
This MASS Document is essential for those who have fundamental knowledge of Scala, Chisel and SoC hardware.
Only the keyword name is used in the MASS Document, but its meaning is stated in the keywords Appendix-Scala & Chisel.

## Slide 27: Aghaz(آغاز) SoC The Beginning

## Slide 28: Specifications of Aghaz(آغاز) SoC
RV-32 (32-bit)
I, M & C extensions
64-KB Instruction and Data Cache
CLINT
PLIC
Privileged( Machine)

## Slide 29: Configuring the AGHAAZ SoC and Core
Create a Aghaaz Core Class with requisite configuration
Add the Aghaaz Core class in the System configuration

## Slide 30: Configuring Aghaz Core in Rocket-Chip
Rocket-Core parameters
Data Cache parameters
Instruction Cache parameters
Class named AghazCore, contains the configurations for the core level functionality. This class is created in Rocket-chip/src/main/scala/subsystem/Config.scala
Path to Default Configuration Scala File

## Slide 31: Configuring RV32IMC Core
RocketCoreParams has the parameters for configuring our Core.
We added MulDiv(Multiplier) with MulDivParmas, having default values, in the RocketCoreParams, in order to enable M extension in our Core.
We updated the value of useAtomics to false, to disable A extension.
The number of cycles per multiplication.
mulEarlyOut will make the multiplier's latency data-dependent, i.e., it will take fewer cycles to multiply small numbers than large ones.
divEarlyOut is analogous to mulEarlyOut (smaller numbers divide more quickly than larger ones).
We updated fpu (Floating-Point unit) to None, to disable F and D extensions in our core.

## Slide 32: Aghaz Core Params (Core)
In the RocketCoreParams, useCompressed is true, means C extension is enabled by default.
Extension I is the base extension and is supported by default as well.
Hence, Aghaz core is configured to support I, M and C Extensions.
useCompressed | true | useCompressed is for C-extension, it is true by default, means our Core will have C-extension enabled implicitly.

## Slide 33: Configuring the icache and dcache in Aghaz Core
Dcache has DCacheParams, which set the parameters for Data Cache.
Similarly, ICache has ICacheParams, which are parameters for the InstructionCache configuration.

## Slide 34: Data Cache Parameters
Parameters | Value | Description
nMSHRs | 0 | There are 0 MSHRs (Miss Status Handling Registers) in Instruction Cache
nWays | 16 | There are 16 Ways of Cache in DCache
nSets | 64 | There are 64 Sets of Cache in DCache
blockBytes | 64 (evaluated) | There are 64 blockBytes in DCache
Instruction Cache Parameters
Parameters | Value | Description
nWays | 4 | There are 4 Ways of Cache in ICache
nSets | 256 | There are 256 Sets of Cache in ICache
blockBytes | 64 (evaluated) | There are 64 blockBytes in ICache
Size of DCache is calculated by: nWays x nSets x blockBytes (16 x 64 x 64 == 64KB)
Size of ICache is calculated by: nWays x nSets x blockBytes (4 x 256 x 64 == 64KB)

## Slide 35: Blocks of Core
Aghaz Core provides extensions for I, M and C with 32bit compatibility.

## Slide 36: How did we know, which parameter is doing what?
The MAS Document describes the parameters, their description, and the modules that are managed by that parameter.

## Slide 37: Blocks of Tile
Rocket-Tile of Aghaz SoC contains Aghaz Core, Branch Target Buffer, L1 Icache & DCache of 64-KB.

## Slide 38: Initializing Aghaz Core to Default Configuration
The class called oldDefaultConfig is inherited by the class Config.
The Class Config (Parent Class) includes the key configurations, from which all configurations must be inherited.
The AghazCore object is generated as a parameter with ’1’ indicating that there is only one(1) core in our AghazCore.
The AghazCore object is further added to the WithCoherentBusTopology object, which includes configurations for the Bus level.
These objects are further added by the newBaseConfig object, which contains the base configurations.
Default Configuration is created in Rocket-chip/src/main/scala/system/Config.scala
Path to Default Configuration Scala File

## Slide 39: Customizing AghazCore to 32-bit Configuration

## Slide 40: Blocks of SoC

## Slide 41: At this point our Aghaz SoC is successfully configured and ready to be built

## Slide 42: Configuring an SoC to your Requirements in a quick process by means of this MAS Document

## Slide 43: Acknowledgements This Document was made possible with the counselling, guidance and support of Dr.Roomi Naqvi, Dr Ali Ahmed Ansari, and Farhan Ahmed Karim. Without their encouragement and guidance, this could not be possible. This Document was created under the Lead of Uzair Khan, along with the team of collaborators/ interns under him that gave their level best under the supervision of such experienced mentors.
Team Members
Waleed Waseem
Shahzaib Kashif
Talha Ahmed
Mohsin Raza
Muhammad Shahzaib
Syeda Fizza Jaffery
Almas Ibrahim
Ubab Nadeem

## Slide 44
December 8-10 | Virtual Event
Thank you for joining us.
Contribute to the RISC-V conversation on social!
#RISCVSUMMIT @risc_v

## Slide 45
https://docs.boom-core.org/en/latest/sections/intro-overview/rocket-chip.html